## Slide 1: Can route charging incentivise environmentally-friendly trajectories?
Tatjana Bolic
SESAR Innovation Days
12 – 15 November 2024

## Slide 2: Outline
Current route charging
Green Route Charging Solution
Climate hotspots
SP Survey
Conclusions

## Slide 3: Route charging today
Charge “is a levy that is designed and applied specifically to recover the costs of providing facilities and services for civil aviation.” ICAO Doc9082
Route per State Overflown (RSO)
  each State crossed implies a route charge to be paid to the State
Unit rate ui is set for each charging zone i
  Unit Rate is a unique tariff per 100 km
Route charge for a flight is a sum of charges accrued over all crossed charging zones i
Where route charge in zone i is a product of the unit rate ui and the amount of service units n “consumed”

## Slide 4: Route charging today
Service units are a product of distance (di) and weight (wi) factors
The distance factor is proportional to the great-circle distance (GCD) between entry and exit points to the charging zone
  if the origin or destination airports are within the charging zone
    distance is GCD from entry point to the airport coordinates, minus 20 km (for arrival airport)
Weight factor takes the maximum take-off weight into account

## Slide 5: Unintended consequences
Longer flights to save on route charges
  about 10% of operational costs
Increase emissions
Congestion
When planning flights do not need to take care of capacity
  nor is the info available to airlines
  active regulation is a proxy of delay

## Slide 6: Green Route Charging (GRC) Solution
Propose business and operational incentivisation of climate-optimised flight planning through route charging​
AUs free to choose trajectory but the most environmentally friendly one should have the least direct costs​
Initial GRC
  Takes into account CO2 and congestion
Full GRC
  Takes into account all aviation emissions
Radiation change
Warming
Cooling
Based on Lee et al. 2009
Grewe et al. (2017,2019)

## Slide 7: Full GRC Solution
Full GRC:
Where the crossing of a climate hotspot would entail an increase of route charges (e.g. a modulation) and avoidance would entail some form of compensation (‘rebate’) in terms of lower route charges for avoiding the hotspot
Two components:
  Climate hotspots
  Airlines’ willingness to pay

## Slide 8: Climate hotspots
Radiative forcing of aviation
  about one-third CO2 effects, and
  about two-thirds non-CO2 effects
Contrails represent largest single contribution of non-CO2 impacts
  large uncertainty
Non-CO2 effects strongly depend on the state of the atmosphere
Climate hotspot
  is a volume of airspace where the atmospheric conditions are such that flying through it creates much higher climate impact
CLIMaCCF and ERA5 data

## Slide 9: Climate hotspots
December 03 2019, 95th percentile
December 03 2019, 99th percentile

## Slide 10: Climate hotspots

## Slide 11: Stated preference survey
Stated preference:
Respondents state their values / preferences, rather than inferring values from actual choices in revealed preference
Revealed preference has disadvantages:
  typically based on executed trajectories
  weakly capable of evaluating future choice sets
  based on weaker inference
Adaptive SP
  subsequent choices dependent on previous ones
We are interested in 4 attributes:
  cost sensitivity: fuel and route charges - 7 levels,
  short arrival delay aversion: 50th percentile delay time – 3 levels,
  long arrival delay tolerance: 90th percentile delay time – 4 levels,
  environmental consideration: environmental impact – 3 levels
Survey is composed of:
  introduction and demographics
  screen and attribute identification tasks
  choice tasks

## Slide 12: SP survey

## Slide 13: SP survey
Consortium members provided 20 responses
Value of time
  Assumes a comparison of an expected arrival delay compared to a certain value of cost
Two delay related variables, testing the adversity of airlines
  to short, relatively certain delays - median
  and long, quite uncertain delays - 90th percentile
Test results – value of time, risk aversion

## Slide 14: SP results
Three models:
  I: cost + expected delay
  II: cost + expected delay + uncertainty
  III: cost + expected delay + uncertainty + environmental impact
Estimation
Value of time and risk aversion:
Different airline types:

## Slide 15: Conclusions
Addressing total climate impact
Two components analysed
SP survey completed
  Utilities being defined
Climate impact
  need to agree on the definition
  a hotspot may be very easily avoided by changing the FL
  hotspots are particularly dynamic, which presents a challenge
Need to define the modulations and rebates
Need to incorporate into the model to assess the new route charging scheme