## Slide 1: Reconciling flexibility and predictability in strategic flight planning
Lorenzo Castelli – University of Trieste
Tatjana Bolić, Andrew Cook – University of Westminster
Research Workshop – Predictability and flexibility
Zagreb, 19 april 2024

## Slide 2: Overview
Current flight and capacity planning
ADAPT objectives
Models and model testing
Data Visualisation Tool

## Slide 3: Current flight and capacity planning in the European ATM system
Airlines
  Schedule known six months ahead

## Slide 4: Current flight and capacity planning in the European ATM system
Initial roster
12 months ahead
Initial capacity
Initial flight plan
120-3 hours ahead
Day of operations
Demand – capacity imbalance
Delay
No need to consider airspace capacity
Airlines
  Schedule known six months ahead
  Trajectory planning flexible
ANSPs
  Initial rosters
  Updates
Updates
Historical traffic

## Slide 5: ADAPT objectives
ADAPT designed and tested models
  Provide information on flight flexibility and saturated portions of airspace
  Could enable strategic collaborative planning
To enhance predictability while at the same time preserving and quantifying flexibility
  Predictability through earlier fully shared information on trajectories and airspace capacities
  Flexibility expressed as Time Windows (TW)
Notes: Predictability is a result of earlier flight planning based on fully shared information on trajectories and airspace capacities.

## Slide 6: Time Window
The TW is checked for entry into each sector/airport
The smallest TW along the trajectory is assigned to the flight
The duration delineates the degree of flexibility granted to the flight
Assigned departure time/
Sector entry time

## Slide 7: Two modelling steps
  Assign a trajectory to each scheduled flight:
      Strategic Air Traffic Assignment model
          Trajectories
          Scheduled departure times (TW opening times)
              Respect the capacity of the network
              Minimise flights’ operational costs
              Guarantee predictability and flexibility
  Quantify flexibility
      Time Windows model (TW duration)

## Slide 8
…
…
…
…
Models
T. Bolić, L. Castelli, L. Corolli, G. Scaini (2021) Flexibility in strategic flight planning, Transportation Research Part E: Logistics and Transportation Review, 154, 102450.
T. Bolić, L. Castelli, G. Scaini, G. Frau, S. Guidi (2021) Flight flexibility in strategic traffic planning: visualisation and mitigation use case, CEAS Aeronautical Journal, 12(4), 847-862.

## Slide 9: Model testing
One day of real air traffic data (DDR2) – 1 September 2017
  30 000 flights
    Aircraft type
    Departure times
    Trajectory options
  Airspace configuration
    As on a day
  Costs

## Slide 10: Results
Models work on this scale
Acceptably fast for strategic/pre-tactical time horizon
What can we see from them?

## Slide 11: Data visualisation tool
Constrained flight - the duration of its TWs is shorter than the maximum allowed duration (15 min)
Saturated (critical) sector-hour - the capacity limit has been reached
Criticality index - measures the degree of criticality of a sector-hour as the total additional number of the time periods that all flights constrained by the same sector-hour would have if it had sufficient capacity

## Slide 14
ADAPT project website:
  https://adapt-h2020.eu/
ADAPT Data Visualisation Tool:
  https://visualization.adapt-h2020.eu/
Lorenzo Castelli – castelli@units.it